V8 Digital Temperature Controller

Features of Function:

It is a mini-sized and integrated intelligent controller

The main functions are: Temperature Display/Temperature Control/Value Storing/Self Testing

Front Panel Operation:

1, Set temperature adjustment:

Press SET button, the set temperature is displayed. Press SET button again to select work②/work① temperature setup.

Press + or - button to modify the temperature. Press OK button to store the displayed value, exit the adjustment and display the cold room temperature.

If no more button is pressed within 10 seconds, the cold room temperature will be displayed.

2, Output LED: During heating, the output LED is on; When the temp. is constant, the output LED is off.

3, Parameter setup:

Press synchronously + and - button, and hold for 3 seconds to enter the parameter setup mode while F1 displayed.

Press +/- button to select F1/F2

Press SET button to select sequentially from the parameters: F12/F13/F14; F22/F23/F24

Press +/- button, the value of parameters will be displayed and can be modified

Press OK button to store the value of parameters; If no more button is pressed within 10 seconds, the value of parameters will be stored automatically, and the cold room temperature displayed

| Parameters | Function | Set range | Default |
| --- | --- | --- | --- |
| F1 1st circuit | F12 | Temp. hysteresis | 1-50℃ | 3℃ |
|  | F13 | Start delay time | 0-10Min | 0Min |
|  | F14 | Offset on room Temp. | -20 ~ 20℃ | 0℃ |
| F2 2nd circuit | F22 | Temp. hysteresis | 1-50℃ | 3℃ |
|  | F23 | Start delay time | 0-10Min | 0Min |
|  | F24 | Offset on room Temp. | -20 ~ 20℃ | 0℃ |

Warnings:

1, The sensor cable leads must be kept separately from main voltage wires in order to avoid high frequency noise induced. Separate the power supply of the loads from the power supply of the controller.

2, All wiring changes must be performed without power supply

3, The temperature controller can not be installed in the area with water drops or excessive humidity; Can not be used under the condition with high temperature, strong electromagnetic interference and strong corrosivity.